## Slide 1
Cycloid
P
C

## Slide 2
Steps to construct cycloid:
1.Draw a rolling circle with specified diameter/radius and plot point C as a center point and P as a base base point.
B
2. From a point P draw a straight line which is equal to circumference of a rolling circle (
P
C
3. Draw horizontal line from point C which is parallel to the straight line passing through point P
4. Divide the circle into equal number of parts
And assign numbers as shown in fig.
1
2
3
4
5
6
7
8
9
10
11
4. Divide straight line passing through point P and C into equal number of parts And assign numbers as shown in fig.
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
C11
C12
5. Draw horizontal lines from each point of circle.
6. Take C1 as a center and radius of a rolling circle mark the arc point on a line which is passing through point 1
7. Take C2 as a center and radius of a rolling circle mark the arc point on a line which is passing through point 2
8. Repeat above steps i.e. step 6 and 7 for all points (upto C12)
9. Joint all points and draw cycloid.

## Slide 3
Problem 1 :

## Slide 4
Epicycloid
O
Directrix circle
P
C
Ꝋ
Ꝋ = radius of rolling circle ( r ) / radius of directrix circle ( R )
Rolling circle

## Slide 5
Steps to construct epicycloid:
1. specify a point O and draw one horizontal line
2. Calculate angle by using following formula
Ꝋ = ( r / R ) X 360
3. From Point O mark the calculated angle and draw line.
5. Mark radius distance of rolling circle from point P
13. Joint all points and draw cycloid.
O
Ꝋ
P
C
6. Draw rolling circle with specified radius and C as a center point.
7. Draw an arc from point C with O as a center.
8. Divide rolling circle and an arc which is passing through point C into equal number of parts and assign numbers.
1
2
4
5
6
7
10
11
3
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
C11
9. Draw an arc from each point of rolling circle.
4. Draw directrix circle with specified radius and O as a center point. also plot point P
8
12. Repeat above steps i.e. step 6 and 7 for all points (upto C12)
10. C1 as a center and radius equal to rolling circle and mark the point on arc passing through point 1
11. C2 as a center and radius equal to rolling circle and mark the point on arc passing through point 2
9

## Slide 6
Problem 1 :