## Slide 1
Arc of circle method :

## Slide 2
Arc of circle method :
Minor Axis
Major Axis
F1
F2

## Slide 3
Steps to construct an ellipse using arc of circle method :
F1
F2
1.Draw major axis AB
A
D
2. Draw minor axis CD
C
4. Plot foci of points F1 and F2
Distance between fixed points is not given
Take radius of OA and C as a centre and mark both side on AB axis.
3. Assign name for intersection point of both axis is ‘O’
O
B
With same radius, now take D as a centre again mark both side on AB
Assign name for both points F1 and F2
Distance is given then directly plot F1 and F2
5. Divide F1 to O into equal number of parts and assign numbers.
4
1
2
3
5
6
6. Take A-1 as a radius and F1 as a centre point and mark the point both sides.
6.1. Take A-1 as a radius and F2 as a centre point and mark the point both sides.
7. Take B-1 as a radius and F1 as a centre point and mark the point both sides.
7.1. Take B-1 as a radius and F2 as a centre point and mark the point both sides.
8. Repeat above four steps i.e. from 6 to 7.1 for all division points

## Slide 4
Problem 1 :
The major axis of an ellipse is 150 mm long and minor axis is 100 mm long. Find Foci and draw an ellipse by ‘Arc of circle method’
Given data : Major Axis AB = 150 mm , Minor Axis CD = 100 mm
Problem 2 :
The major axis of an ellipse is 100 mm long and minor axis is 70 mm long. Find Foci and draw an ellipse by ‘Arc of circle method’
Given data : Major Axis AB = 100 mm , Minor Axis CD = 70 mm