## Slide 1
Concentric circle method :

## Slide 2
Steps to construct an ellipse using concentric circle method :
1.Draw a circle with diameter which is equal to major axis
2. Draw another circle with diameter which is equal to minor axis
B
4. Draw both Axis as perpendicular by sector of each other
Let major axis be AB and minor axis be CD
3. Assign name for center point is ‘O’
5. Divide both the circle into 12 equal parts
6. From all points of outer circle draw vertical lines downwards and upwards respectively
O
A
B
D
C
Methods to divide circle into equal parts (outer circle)
Method 1 : at center point O mark 30 degree angle because 360/12
Method 2 : take OB as a radius and B as a center point and mark both side on outer circle. Similarly with same radius i.e.(OB) from each point i.e. C,A,D (outer circle) mark the points both side.
Name the as shown in figure.
4
8
2
3
5
6
9
10
11
12
1
7
8
2
3
5
6
9
11
12
7. From all points of outer circles draw horizontal lines those intersect vertical lines.
8. Mark all the points.
9. Joint all points and draw an ellipse.

## Slide 3
Problem 1 :
The major axis of an ellipse is 100 mm long and minor axis is 70 mm long. Draw an ellipse by ‘Concentric Circle Method’
Given data : Major Axis AB = 100 mm , Minor Axis CD = 70 mm

## Slide 4
Rectangle method :

## Slide 5
Steps to construct an ellipse using concentric circle method :
1.Draw Major Axis and Minor Axis AB and CD
2. Connect all points and draw EFGH rectangle
B
4. Divide AO into equal number of parts
3. Assign name for center point is ‘O’
5. Divide AE into equal number of parts.
7. Join point D-1, D-2, D-3, D-4 and extend.
A
B
D
C
E
F
G
H
O
6. Assign name for all points as shown in figure.
1
2
3
4
1’
2’
3’
4’
8. Join point C-1’, C-2’, C-3’, C-4’ and extend.
9. Mark point P1,P2,P3,P4 which obtain by intersection of C-1’ and D-1 and so on.
P1
P2
P3
P4
10. Divide AH into equal number of parts.
11. Draw horizontal lines from each division points
12. Draw vertical lines from P1,P2,P3,P4 extend it as shown in fig.
13. Joint all points and draw an ellipse.