## Slide 1
Involute
Involute is a single curved line traced out by an end of a string when unwound itself from a circle.

## Slide 2
Steps to construct involute of a circle:
1. Draw a circle according to given diameter
2. from the base point draw a string line and length of this line is equal to circumference of circle i.e. ∏D and plot point P.
P
3 . Divide circle and string length into equal number of parts and assign numbers as shown in fig.
1
2
3
4
5
6
7
8
9
10
11
12
1’
2’
3’
4’
5’
6’
7’
8’
9’
10’
11’
12’
4 . Draw tangent from point 1 to 12 ( 90 degree angle)
5 . Take a radius P to 1’ and Point 1 as a center point and mark a point on first line which is passing through point 1 of a circle.
6 . Take a radius P to 2’ and Point 2 as a center point and mark a point on first line which is passing through point 2 of a circle.
7 . Repeat above steps for all points and joint

## Slide 3
Steps to construct involute of a square:
1. Draw a square according to given length and assign name
2. from the point B draw a string line and length of this line is equal to perimeter of square i.e. 4 X side of square
3 . Draw straight line from each point
4 . Mark a point on line extended by Point A with length of AB
5 . Mark a point on line D such that length is equal to AB +AD
6 . Mark a point on line C such that length is equal to AB +AD + DC
A
B
C
D
7 . Mark a point on line B such that length is equal to AB +AD + DC +BC

## Slide 4
Problem 1 :
Construct involute of a circle of diameter 30 mm. String length is equal to circumference of a circle.
Problem 2 :
Construct involute of a Square with 30 mm side.